## Slide 1: Implementing Virtual Private Networks

## Slide 2: VPN Terminology

## Slide 3: Cryptosystem
A system to accomplish the encryption/decryption, user authentication, hashing, and key-exchange processes.
A cryptosystem may use one of several different methods, depending on the policy intended for various user traffic situations.

## Slide 4: Encryption / Decryption
Encryption transforms information (clear text) into ciphertext which is not readable by unauthorized users.
Decryption transforms ciphertext back into clear text making it readable by authorized users.
Popular encryption algorithms include:
  DES
  3DES
  AES

## Slide 5: Authentication / Hashing
Guarantees message integrity by using an algorithm to convert a variable length message and shared secret key into a single fixed-length string.
Popular hashing methods include:
  SHA (Cisco default)
  MD5

## Slide 6: Non-repudiation
Is the ability to prove a transaction occurred.
  Similar to a signed package received from a shipping company.
This is very important in financial transactions and similar data transactions.

## Slide 7: Diffie-Hellman Key Exchange
How do the encrypting and decrypting devices get the shared secret key?
  The easiest method is Diffie-Hellman public key exchange.
Used to create a shared secret key without prior knowledge.
This secret key is required by:
  The encryption algorithm (DES, 3DES, AES)
  The authentication method (MD5 and SHA-1)

## Slide 8: Pre-Shared Key
Identifies a communicating party during a phase 1 IKE negotiation.
The key must be pre-shared with another party before the peers routers can communicate.

## Slide 9: IPsec - Internet Protocol Security
A “framework” of open standards developed by the IETF to create a secure tunnel at the network (IP) layer.
  It spells out the rules for secure communications.
IPsec is not bound to any specific encryption or authentication algorithms, keying technology, or security algorithms.

## Slide 10: IPsec Protocol Framework

## Slide 11: Crypto Map
A Cisco IOS software configuration entity that performs two primary functions.
  First, it selects data flows that need security processing.
  Second, it defines the policy for these flows and the crypto peer that traffic needs to go to.
A crypto map is applied to an interface.

## Slide 12: SA - Security Association
Is a contract between two parties indicating what security parameters, such as keys and algorithms will be used.
A Security Parameter Index (SPI) identifies each established SA.

## Slide 13: Cryptography Names
Alice and Bob
  Are commonly used placeholders in cryptography.
  Better than using Person A and Person B
  Generally Alice wants to send a message to Bob.
Carol or Charlie
  A third participant in communications.
Dave is a fourth participant, and so on alphabetically.
Eve
  An eavesdropper, is usually a passive attacker.
  She can listen in on messages but cannot modify them.
Mallory or Marvin or Mallet
  A malicious attacker which is more difficult to monitor.
  He/She can modify and substitute messages, replay old messages, etc.
Walter
  A warden to guard Alice and Bob depending on protocol used.

## Slide 14: VPNs

## Slide 15: Conventional Private Networks

## Slide 16: Virtual Private Networks

## Slide 17: VPNs
A Virtual Private Network (VPN) provides the same network connectivity for remote users over a public infrastructure as they would have over a private network.
VPN services for network connectivity include:
  Authentication
  Data integrity
  Confidentiality

## Slide 18: Characteristics of VPNs

## Slide 19: VPN Concepts
A secure VPN is a combination of concepts:

## Slide 20: VPN Packet Encapsulation

## Slide 21: VPN Packet Encapsulation

## Slide 22: VPN Topologies

## Slide 23: Two Types of VPNs
Site-to-Site VPNs:
  Intranet VPNs connect corporate headquarters, remote offices, and branch offices over a public infrastructure.
  Extranet VPNs link customers, suppliers, partners, or communities of interest to a corporate Intranet over a public infrastructure.
Remote Access VPNs:
  Which securely connect remote users, such as mobile users and telecommuters, to the enterprise.

## Slide 24: Site-to-Site VPNs
Notes: Site-to-site VPNs provide cost benefits relative to private WANs and also enable new applications like extranets. However, site-to-site VPNs are still an end-to-end network and are subject to the same scalability, reliability, security, multi-protocol, etc. requirements that exist in the private WAN. In fact, since VPN are built on a public network infrastructure, they have additional requirements such as heightened security, advanced QoS capabilities, and a set of policy management tools to manage these additional features.
Cisco provides a suite of VPN-optimized routers. Cisco IOS software running in Cisco routers combines rich VPN services with industry-leading routing, thus delivering a comprehensive solution. Cisco routing software adds scalability, reliability, multi-protocol, multi-service, management, Service Level Agreement monitoring, and QoS to site-to-site applications. The Cisco VPN software adds strong security via encryption and authentication. This Cisco VPN-based products provide high performance for site-to-site, intranet and extranet, VPN solutions.

## Slide 25: Site-to-Site VPNs

## Slide 26: Remote Access VPNs

## Slide 27: Remote Access VPNs

## Slide 28: Remote Access VPNs

## Slide 29: Cisco VPN Product Line
Secondary role
Primary role
Home Routers (Linksys, D-Link, …)
Secondary role
Primary role
Cisco VPN 3000 Series Concentrators
Secondary role
Primary role
Cisco ASA 5500 Adaptive Security Appliances
Secondary role
Secondary role
Remote-Access VPN
Primary role
Cisco VPN-Enabled Router
Primary role
Cisco PIX 500 Series Security Appliances (Legacy)
Site-to-Site VPN
Product Choice

## Slide 30: GRE Tunnel

## Slide 31: Layer 3 Tunneling
There are 2 popular site-to-site tunneling protocols:
  Cisco Generic Routing Encapsulation (GRE)
  IP Security Protocol (IPsec)
When should you use GRE and / or IPsec?
User Traffic
IP Only?
Use GRE Tunnel
No
Yes
No
Yes
Unicast Only?
Use IPsec VPN

## Slide 32: Generic Routing Encapsulation (GRE)
GRE can encapsulate almost any other type of packet.
  Uses IP to create a virtual point-to-point link between Cisco routers
  Supports multiprotocol (IP, CLNS, …) and IP multicast tunneling (and therefore routing protocols)
  Best suited for site-to-site multiprotocol VPNs
  RFC 1702 and RFC 2784
GRE header adds 24 bytes of additional overhead

## Slide 33: Optional GRE Extensions
GRE can optionally contain any one or more of these fields:
  Tunnel checksum
  Tunnel key
  Tunnel packet sequence number
GRE keepalives can be used to track tunnel path status.

## Slide 34: Generic Routing Encapsulation (GRE)
GRE does not provide encryption!
  It can be monitored with a protocol analyzer.
However, GRE and IPsec can be used together.
IPsec does not support multicast / broadcast and therefore does not forward routing protocol packets.
  However IPsec can encapsulate a GRE packet that encapsulates routing traffic (GRE over IPsec).

## Slide 35: Five Steps to Configuring a GRE Tunnel
Create a tunnel interface: interface tunnel 0
Assign the tunnel an IP address.
Identify the source tunnel interface: tunnel source
Identify the tunnel destination: tunnel destination
(Optional) Identify the protocol to encapsulate in the GRE tunnel: tunnel mode gre ip
  By default, GRE is tunneled in an IP packet.

## Slide 36: Five Steps to Configuring a GRE Tunnel
R1(config)# interface tunnel 0
R1(config–if)# ip address 10.1.1.1 255.255.255.252
R1(config–if)# tunnel source serial 0/0
R1(config–if)# tunnel destination 209.165.200.225
R1(config–if)# tunnel mode gre ip
R1(config–if)#
R2(config)# interface tunnel 0
R2(config–if)# ip address 10.1.1.2 255.255.255.252
R2(config–if)# tunnel source serial 0/0
R2(config–if)# tunnel destination 209.165.201.1
R2(config–if)# tunnel mode gre ip
R2(config–if)#

## Slide 37: GRE Tunnel Example

## Slide 38: IPsec

## Slide 39: IPsec - Internet Protocol Security
A “framework” of open standards developed by the IETF to create a secure tunnel at the network (IP) layer.
  It spells out the rules for secure communications.
  RFC 2401 - RFC 2412
IPsec is not bound to any specific encryption or authentication algorithms, keying technology, or security algorithms.
IPsec allows newer and better algorithms to be implemented without patching the existing IPsec standards.

## Slide 40: IPsec Protocol Framework
AH
ESP
ESP + AH
DES
3
DES
AES
SEAL
MD5
SHA
PSK
RSA
DH1
DH2
DH5
DH7

## Slide 41: IPsec Protocol Framework

## Slide 42: Confidentiality

## Slide 43: Integrity

## Slide 44: Authentication

## Slide 45: Secure Key Exchange
AH
ESP
ESP + AH
DES
3
DES
AES
SEAL
MD5
SHA
PSK
RSA
DH1
DH2
DH5
DH7
768 bits
1024 bits
1536 bits
Used by DES and 3DES
Used by AES

## Slide 46: IPsec Framework Protocols
IPsec uses two main protocols to create a security framework:
  AH: Authentication Header
  ESP: Encapsulating Security Payload

## Slide 47: Authentication Header (AH)
AH provides authentication and optional replay-detection services.
  It authenticates the sender of the data.
  AH operates on protocol number 51.
  AH supports the HMAC-MD5 and HMAC-SHA-1 algorithms.

## Slide 48: Authentication Header (AH)
AH does not provide confidentiality (encryption).
  It is appropriate to use when confidentiality is not required or permitted.
  All text is transported unencrypted.
It only ensures the origin of the data and verifies that the data has not been modified during transit.
If the AH protocol is used alone, it provides weak protection.
AH can have problems if the environment uses NAT.

## Slide 49: Encapsulating Security Payload (ESP)
ESP provides the same security services as AH (authentication and integrity) AND encryption service.
  It encapsulates the data to be protected.
  It operates on protocol number 50.

## Slide 50: Encapsulating Security Payload (ESP)
ESP can also provide integrity and authentication.
  First, the payload is encrypted using DES (default), 3DES, AES, or SEAL.
  Next, the encrypted payload is hashed to provide authentication and data integrity using HMAC-MD5 or HMAC-SHA-1.

## Slide 51: Transport Mode and Tunnel Mode
ESP and AH can be applied to IP packets in two different modes.

## Slide 52: Transport Mode
Security is provided only for the Transport Layer and above.
  It protects the payload but leaves the original IP address in plaintext.
ESP transport mode is used between hosts.
Transport mode works well with GRE, because GRE hides the addresses of the end devices by adding its own IP.

## Slide 53: Tunnel Mode
Tunnel mode provides security for the complete original IP packet.
  The original IP packet is encrypted and then it is encapsulated in another IP packet (IP-in-IP encryption).
ESP tunnel mode is used in remote access and site-to-site implementations.

## Slide 54: Key Exchange

## Slide 55: Key Exchange
The IPsec VPN solution:
  Negotiates key exchange parameters (IKE).
  Establishes a shared key (DH).
  Authenticates the peer.
  Negotiates the encryption parameters.
The negotiated parameters between two devices are known as a security association (SA).

## Slide 56: Security Associations (SAs)
SAs represent a policy contract between two peers or hosts, and describe how the peers will use IPsec security services to protect network traffic.
SAs contain all the security parameters needed to securely transport packets between the peers or hosts, and practically define the security policy used in IPsec.

## Slide 57: SA Security Parameters

## Slide 58: IKE - Internet Key Exchange
IKE helps IPsec securely exchange cryptographic keys between distant devices.
  Combination of the ISAKMP and the Oakley Key Exchange Protocol.
Key Management can be preconfigured with IKE (ISAKMP) or with a manual key configuration.
  IKE and ISAKMP are often used interchangeably.
The IKE tunnel protects the SA negotiations.
  After the SAs are in place, IPsec protects the data that Alice and Bob exchange.

## Slide 59: How IPsec uses IKE
Outbound packet is sent from Alice to Bob. No IPsec SA.
Packet is sent from Alice to Bob protected by IPsec SA.
IPsec
IPsec

## Slide 60: IKE - Internet Key Exchange
There are two phases in every IKE negotiation
  Phase 1 (Authentication)
  Phase 2 (Key Exchange)
IKE negotiation can also occur in:
  Main Mode
  Aggressive mode
The difference between the two is that Main mode requires the exchange of 6 messages while Aggressive mode requires only 3 exchanges.

## Slide 61: IKE Main Mode Phases
IKE Phase One:
  Negotiates an IKE protection suite.
  Exchanges keying material to protect the IKE session (DH).
  Authenticates each other.
  Establishes the IKE SA.
  Main Mode requires the exchange of 6 messages while Aggressive mode only uses 3 messages.
IKE Phase Two:
  Negotiates IPsec security parameters, known as IPsec transform sets.
  Establishes IPsec SAs.
  Periodically renegotiates IPsec SAs to ensure security.
  Optionally performs an additional DH exchange.

## Slide 62: IKE Phases

## Slide 63: Five Steps of IPsec
IKE Phase 1 authenticates IPsec peers and negotiates IKE SAs to create a secure communications channel for negotiating IPsec SAs in Phase 2.
Host A sends interesting traffic destined for Host B.
IKE Phase 2 negotiates IPsec SA parameters and creates matching IPsec SAs in the peers to protect data and messages exchanged between endpoints.
Data transfer occurs between IPsec peers based on the IPsec parameters and keys stored in the SA database.
IPsec tunnel termination occurs by SAs through deletion or by timing out.
Step 1
Step 2
Step 3
Step 4
Step 5

## Slide 64: Step 1 – Interesting Traffic

## Slide 65: Step 2 – IKE Phase 1
IKE Policy Negotiation

## Slide 66: Step 2 – IKE Phase 1
DH Key Exchange
RouterB hashes the received string together with the pre-shared secret and yields a hash value.
RouterA randomly chooses a string and sends it to RouterB.
RouterB sends the result of hashing back to RouterA.
RouterA calculates its own hash of the random string, together with the pre-shared secret, and matches it with the received result from the other peer.
If they match, RouterB knows the pre-shared secret, and is considered authenticated.

## Slide 67: Step 2 – IKE Phase 1
DH Key Exchange
Now RouterB randomly chooses a different random string and sends it to RouterA.
RouterA also hashes the received string together with the pre-shared secret and yields a hash value.
RouterA sends the result of hashing back to RouterB.
RouterB calculates its own hash of the random string, together with the pre-shared secret, and matches it with the received result from the other peer.
If they match, RouterA knows the pre-shared secret, and is considered authenticated.

## Slide 68: Step 2 – IKE Phase 1
Peer Authentication

## Slide 69: Step 3 – IKE Phase 2
IPsec Negotiation

## Slide 70: Step 3 – IKE Phase 2
Transform Set Negotiation

## Slide 71: Step 3 – IKE Phase 2
Security Associations

## Slide 72: Step 4
IPsec Session

## Slide 73: Step 5
Tunnel Termination

## Slide 74: IPsec Tasks

## Slide 75: IPsec Tasks
Ensure that ACLs configured on the interface are compatible with IPsec configuration.
Create an IKE policy to determine the parameters that will be used to establish the tunnel.
Configure the IPsec transform set which defines the parameters that the IPsec tunnel uses.
  The set can include the encryption and integrity algorithms.
Create a crypto ACL.
  The crypto ACL defines which traffic is sent through the IPsec tunnel and protected by the IPsec process.
Create and apply a crypto map.
  The crypto map groups the previously configured parameters together and defines the IPsec peer devices.
  The crypto map is applied to the outgoing interface of the VPN device.

## Slide 76: IKE and IPsec Flowchart
1
2
3

## Slide 77: Ensure the Network Works

## Slide 78: Task 1: Ensure ACLs are Compatible
ESP = protocol # 50, AH = protocol # 51, ISAKMP = UDP port 500

## Slide 79: Task 2: Configure IKE
Creating a plan in advance is mandatory to configure IPsec encryption correctly to minimize misconfiguration.
Determine the following policy details:
  Key distribution method
  Authentication method
  IPsec peer IP addresses and hostnames
  IKE phase 1 policies for all peers
  Encryption algorithm, Hash algorithm, IKE SA lifetime
Goal: Minimize misconfiguration.

## Slide 80: IKE Phase 1 Policy Parameters
or AES
or D-H 5

## Slide 81: Enable IKE

## Slide 82: Create an IKE Policy

## Slide 83: Default ISAKMP Settings

## Slide 84: Default ISAKMP Settings
RouterA# show crypto isakmp policy
Protection suite of priority 110
encryption algorithm: DES - Data Encryption Standard (56 bit keys).
hash algorithm: Message Digest 5
authentication method: Pre-Shared Key
Diffie-Hellman group: #1 (768 bit)
lifetime: 86400 seconds, no volume limit
Default protection suite
encryption algorithm: DES - Data Encryption Standard (56 bit keys).
hash algorithm: Secure Hash Standard
authentication method: Rivest-Shamir-Adleman Signature
Diffie-Hellman group: #1 (768 bit)
lifetime: 86400 seconds, no volume limit

## Slide 85: Create an IKE Policy

## Slide 86: ISAKMP Policy Negotiation

## Slide 87: ISAKMP Policy Negotiation

## Slide 88: Configure Pre-Shared Keys
By default, the ISAKMP identity is set to use the IP address.

## Slide 89: Configure Pre-Shared Keys

## Slide 90: Configure ISAKMP Identity
To use the hostname parameter, configure the crypto isakmp identity hostname global configuration mode command.
  In addition, DNS must be accessible to resolve the hostname.

## Slide 91: Verify IKE Configuration
RouterA# show crypto isakmp policy
Protection suite of priority 110
encryption algorithm: DES - Data Encryption Standard (56 bit keys).
hash algorithm: Message Digest 5
authentication method: Pre-Shared Key
Diffie-Hellman group: #1 (768 bit)
lifetime: 86400 seconds, no volume limit
Default protection suite
encryption algorithm: DES - Data Encryption Standard (56 bit keys).
hash algorithm: Secure Hash Standard
authentication method: Rivest-Shamir-Adleman Signature
Diffie-Hellman group: #1 (768 bit)
lifetime: 86400 seconds, no volume limit

## Slide 92: Task 3: Configure the Transform Sets
Determine the following policy details:
  IPsec algorithms and parameters for optimal security and performance
  Transforms sets
  IPsec peer details
  IP address and applications of hosts to be protected
  Manual or IKE-initiated SAs
Goal: Minimize misconfiguration.

## Slide 93: IPsec Transforms Supported in IOS
Cisco IOS software supports the following IPsec transforms:
CentralA(config)# crypto ipsec transform-set transform-set-name ?
ah-md5-hmac AH-HMAC-MD5 transform
ah-sha-hmac AH-HMAC-SHA transform
esp-3des ESP transform using 3DES(EDE) cipher (168 bits)
esp-des ESP transform using DES cipher (56 bits)
esp-md5-hmac ESP transform using HMAC-MD5 auth
esp-sha-hmac ESP transform using HMAC-SHA auth
esp-null ESP transform w/o cipher
Note:
  esp-md5-hmac and esp-sha-hmac provide more data integrity.
  They are compatible with NAT/PAT and are used more frequently than ah-md5-hmac and ah-sha-hmac.

## Slide 94: IPsec Policy Example

## Slide 95: Specific IPsec show Commands
RouterA# show crypto isakmp policy Default protection suite encryption algorithm: DES - Data Encryption Standard (56 bit keys) hash algorithm: Secure Hash Standard authentication method: Rivest-Shamir-Adleman Signature Diffie-Hellman Group: #1 (768 bit) lifetime: 86400 seconds, no volume limit
RouterA# show crypto map Crypto Map “MYMAP" 10 ipsec-isakmp Peer = 172.30.2.2 Extended IP access list 102 access-list 102 permit ip host 172.30.1.2 host 172.30.2.2 Current peer: 172.30.2.2 Security association lifetime: 4608000 kilobytes/3600 seconds PFS (Y/N): N Transform sets={ MY-SET, }
RouterA# show crypto ipsec transform-set MY-SET Transform set MY-SET: { esp-des } will negotiate = { Tunnel, },

## Slide 96: Configure Transform Sets

## Slide 97: Transform Set Negotiation

## Slide 98: Transform Set Negotiation

## Slide 99: Configure Security Association Lifetimes
Configures global IPsec lifetime values used when negotiating IPsec security associations.
IPsec SA lifetimes are negotiated during IKE phase 2.

## Slide 100: Task 4: Configure Crypto ACLs
tcp

## Slide 101: Configure Symmetrical Peer Crypto ACL
access-list 110 permit tcp 10.0.1.0 0.0.0.255 10.0.2.0 0.0.0.255
RouterA#(config)
access-list 110 permit tcp 10.0.2.0 0.0.0.255 10.0.1.0 0.0.0.255
RouterB#(config)

## Slide 102: Task 5: Apply the Crypto Map

## Slide 103: Configure IPsec Crypto Maps

## Slide 104: Configure IPsec Crypto Maps

## Slide 105: Configure IPsec Crypto Maps

## Slide 106: Example Crypto Map Commands
RouterA(config)# crypto map MYMAP 110 ipsec-isakmp
RouterA(config-crypto-map)# match address 110
RouterA(config-crypto-map)# set peer 172.30.2.2
RouterA(config-crypto-map)# set peer 172.30.3.2
RouterA(config-crypto-map)# set transform-set MINE
RouterA(config-crypto-map)# set security-association lifetime 86400

## Slide 107: Applying Crypto Maps to Interfaces

## Slide 108: IPsec Configuration Examples

## Slide 109: Verify IPsec

## Slide 110: clear commands
Clears IPsec Security Associations in the router database.
clear crypto sa
clear crypto sa peer <IP address | peer name>
clear crypto sa map <map name>
clear crypto sa entry <destination-address protocol spi>
Router#

## Slide 111: View Policy
RouterA# show crypto isakmp policy
Protection suite of priority 110
encryption algorithm: DES - Data Encryption Standard (56 bit keys).
hash algorithm: Message Digest 5
authentication method: pre-share
Diffie-Hellman group: #1 (768 bit)
lifetime: 86400 seconds, no volume limit
Default protection suite
encryption algorithm: DES - Data Encryption Standard (56 bit keys).
hash algorithm: Secure Hash Standard
authentication method: Rivest-Shamir-Adleman Signature
Diffie-Hellman group: #1 (768 bit)
lifetime: 86400 seconds, no volume limit

## Slide 112: View Defined Sets
E0/1 172.30.1.2
E0/1 172.30.2.2
A
RouterA# show crypto ipsec transform-set MY-SET Transform set MY-SET: { esp-des } will negotiate = { Tunnel, },

## Slide 113: Display Phase 1 SA
QM_IDLE (quiescent state) indicates that an ISAKMP SA exists but is idle.
The router will remain authenticated with its peer and may be used for subsequent quick mode (QM) exchanges.
RouterA# show crypto isakmp sa
dst src state conn-id slot
172.30.2.2 172.30.1.2 QM_IDLE 47 5
E0/1 172.30.1.2
E0/1 172.30.2.2
A

## Slide 114: View Crypto IPsec SA
RouterA# show crypto ipsec sa
interface: Ethernet0/1
  Crypto map tag: MYMAP, local addr. 172.30.1.2
  local ident (addr/mask/prot/port): (172.30.1.2/255.255.255.255/0/0)
  remote ident (addr/mask/prot/port): (172.30.2.2/255.255.255.255/0/0)
  current_peer: 172.30.2.2
  PERMIT, flags={origin_is_acl,}
  #pkts encaps: 21, #pkts encrypt: 21, #pkts digest 0
  #pkts decaps: 21, #pkts decrypt: 21, #pkts verify 0
  #send errors 0, #recv errors 0
  local crypto endpt.: 172.30.1.2, remote crypto endpt.: 172.30.2.2
  path mtu 1500, media mtu 1500
  current outbound spi: 8AE1C9C
E0/1 172.30.1.2
E0/1 172.30.2.2
A

## Slide 115: View Configured Crypto Maps
RouterA# show crypto map
Crypto Map “MYMAP" 10 ipsec-isakmp
  Peer = 172.30.2.2
  Extended IP access list 102
  access-list 102 permit ip host 172.30.1.2 host 172.30.2.2
  Current peer: 172.30.2.2
  Security association lifetime: 4608000 kilobytes/3600 seconds
  PFS (Y/N): N
  Transform sets={ MINE, }
E0/1 172.30.1.2
E0/1 172.30.2.2
A

## Slide 116: Crypto System Error Messages for ISAKMP
To display debug messages about all IPsec actions, use the global command debug crypto ipsec.
To display debug messages about all ISAKMP actions, use the global command debug crypto isakmp.

## Slide 117: Crypto System Error Messages for ISAKMP
ISAKMP SA with the remote peer was not authenticated.
ISAKMP peers failed protection suite negotiation for ISAKMP.
%CRYPTO-6-IKMP_SA_NOT_AUTH: Cannot accept Quick Mode exchange from %15i if SA is not authenticated!
%CRYPTO-6-IKMP_SA_NOT_OFFERED: Remote peer %15i responded with attribute [chars] not offered or changed

## Slide 118: Crypto System Error Messages for ISAKMP
This is an example of the Main Mode error message.
The failure of Main Mode suggests that the Phase I policy does not match on both sides.
Verify that the Phase I policy is on both peers and ensure that all the attributes match.
  Encryption: DES or 3DES
  Hash: MD5 or SHA
  Diffie-Hellman: Group 1 or 2
  Authentication: rsa-sig, rsa-encr or pre-share
1d00h: ISAKMP (0:1): atts are not acceptable. Next payload is 0 1d00h: ISAKMP (0:1); no offers accepted!
1d00h: ISAKMP (0:1): SA not acceptable!
1d00h: %CRYPTO-6-IKMP_MODE_FAILURE: Processing of Main Mode failed with peer at 150.150.150.1

## Slide 119: VPN Lab

## Slide 120: VPN Lab Example
Configuring a Site-to-Site IPsec VPN Using Pre-Shared Keys

## Slide 121: ISP Router
hostname R1
!
interface Serial0/0
ip address 192.168.191.1 255.255.255.0
encapsulation frame-relay
!
interface Serial0/1
ip address 192.168.192.1 255.255.255.0
!
ip route 192.168.0.0 255.255.255.0 192.168.191.2
ip route 192.168.200.0 255.255.255.0 192.168.192.2

## Slide 122: Lab Example
hostname R2
!
crypto isakmp policy 100
authentication pre-share
crypto isakmp key CISCO1234 address 192.168.192.2
!
crypto ipsec transform-set MYSET esp-des
!
crypto map MYMAP 110 ipsec-isakmp
set peer 192.168.192.2
set transform-set MYSET
match address 120
!
interface Serial0/0
ip address 192.168.191.2 255.255.255.0
encapsulation frame-relay
crypto map MYMAP
ip route 0.0.0.0 0.0.0.0 192.168.191.1
!
access-list 120 permit ip 192.168.0.0 0.0.0.255 192.168.200.0 0.0.0.255

## Slide 123: Lab Example
hostname R3
!
crypto isakmp policy 100
authentication pre-share
crypto isakmp key CISCO1234 address 192.168.191.2
!
crypto ipsec transform-set MYSET esp-des
!
crypto map MYMAP 110 ipsec-isakmp
set peer 192.168.191.2
set transform-set MYSET
match address 120
interface Serial0/1
ip address 192.168.192.2 255.255.255.0
clockrate 56000
crypto map MYMAP
!
ip route 0.0.0.0 0.0.0.0 192.168.192.1
!
access-list 120 permit ip 192.168.200.0 0.0.0.255 192.168.0.0 0.0.0.255

## Slide 124: Verify the VPN Configuration
Clear the crypto security associations.
  R2# clear crypto sa
  R2# clear crypto isakmp

## Slide 125: Verify the VPN Configuration
Verify that the IPSEC SAs have been cleared.
  R2# sho crypto ipsec sa
  interface: Serial0/0
  Crypto map tag: MYMAP, local addr. 192.168.191.2
  local ident (addr/mask/prot/port): (192.168.0.0/255.255.255.0/0/0)
  remote ident (addr/mask/prot/port): (192.168.200.0/255.255.255.0/0/0)
  current_peer: 192.168.192.2
  PERMIT, flags={origin_is_acl,}
  #pkts encaps: 0, #pkts encrypt: 0, #pkts digest 0
  #pkts decaps: 0, #pkts decrypt: 0, #pkts verify 0
  #pkts compressed: 0, #pkts decompressed: 0
  #pkts not compressed: 0, #pkts compr. failed: 0, #pkts decompress failed: 0
  #send errors 0, #recv errors 0
  local crypto endpt.: 192.168.191.2, remote crypto endpt.: 192.168.192.2
  path mtu 1500, media mtu 1500
  current outbound spi: 0

## Slide 126: Verify the VPN Configuration
Initiate an extended ping from each respective LAN, to test the VPN configuration.
  R2# ping
  Protocol [ip]:
  Target IP address: 192.168.200.1
  Repeat count [5]:
  Datagram size [100]:
  Timeout in seconds [2]:
  Extended commands [n]: y
  Source address or interface: 192.168.0.1
  Type of service [0]:
  Set DF bit in IP header? [no]:
  Validate reply data? [no]:
  Data pattern [0xABCD]:
  Loose, Strict, Record, Timestamp, Verbose[none]:
  Sweep range of sizes [n]:
  Type escape sequence to abort.
  Sending 5, 100-byte ICMP Echos to 192.168.200.1, timeout is 2 seconds:
  .!!!!
  Success rate is 80 percent (4/5), round-trip min/avg/max = 132/135/136 ms

## Slide 127: Verify the VPN Configuration
After the extended ping, verify IPSEC SAs.
  R2# sho crypto ipsec sa
  interface: Serial0/0
  Crypto map tag: MYMAP, local addr. 192.168.191.2
  local ident (addr/mask/prot/port): (192.168.0.0/255.255.255.0/0/0)
  remote ident (addr/mask/prot/port): (192.168.200.0/255.255.255.0/0/0)
  current_peer: 192.168.192.2
  PERMIT, flags={origin_is_acl,}
  #pkts encaps: 4, #pkts encrypt: 4, #pkts digest 0
  #pkts decaps: 4, #pkts decrypt: 4, #pkts verify 0
  #pkts compressed: 0, #pkts decompressed: 0
  #pkts not compressed: 0, #pkts compr. failed: 0, #pkts decompress failed: 0
  #send errors 1, #recv errors 0
  local crypto endpt.: 192.168.191.2, remote crypto endpt.: 192.168.192.2
  path mtu 1500, media mtu 1500
  current outbound spi: 126912DC

## Slide 128: Configuring IPsec VPN using CCP

## Slide 129: CCP ‘Wizards’
Other intelligent Cisco wizards are available in CCP for these three tasks:
  Auto detecting misconfiguration and proposing fixes.
  Providing strong security and verifying configuration entries.
  Using device and interface-specific defaults.

## Slide 130: CCP ‘Wizards’
Examples of CCP wizards include:
  Startup wizard for initial router configuration
  LAN and WAN wizards
  Policy-based firewall and access-list management to easily configure firewall settings based on policy rules
  IPS wizard
  One-step site-to-site VPN wizard
  One-step router lockdown wizard to harden the router

## Slide 131: VPN Configuration Page

## Slide 132: VPN Configuration Page

## Slide 133: Site-to-Site VPN Components
VPN wizards use two sources to create a VPN connection:
  User input during the step-by-step wizard process
  Preconfigured VPN components
CCP provides some default VPN components:
  IPsec transform set for Quick Setup wizard
Other components are created by the VPN wizards:
  Two IKE policies
Some components (for example, PKI) must be configured before the wizards can be used.

## Slide 134: VPN Configuration Page

## Slide 135: Quick Setup

## Slide 136: Quick Setup

## Slide 137: Quick Setup

## Slide 138: Step-by-Step Setup
Multiple steps are required to configure the VPN connection:
  Defining connection settings: Outside interface, peer address, authentication credentials
  Defining IKE proposals: Priority, encryption algorithm, HMAC, authentication type, Diffie-Hellman group, lifetime
  Defining IPsec transform sets: Encryption algorithm, HMAC, mode of operation, compression
  Defining traffic to protect: Single source and destination subnets, ACL
  Reviewing and completing the configuration

## Slide 139: Configuring Connection Settings
Notes: Configuring Connection Settings
The diagram shows the first task in the step-by-step setup, configuring connection settings:
Choose the outside interface that will be used for traffic going to the IPsec peer over the untrusted network.
Specify the IP address of the peer. This is the reachable next-hop address and not the address of the internal LAN interface.
Choose the authentication method (either Pre-shared keys or Digital Certificates) and specify the credentials. Use long and random pre-shared keys to prevent brute-force and dictionary attacks against IKE.
Click the Next button to proceed to the next task.

## Slide 140: Configuring IKE Proposals
Notes: Configuring IKE Proposals
The second task in the step-by-step setup is to configure IKE proposals using the screen shown:
CCP predefines a default IKE proposal. You can use this IKE proposal (and skip Step 2) or add new proposals.
If you want to use a custom IKE proposal, create one by clicking the Add button and specifying the required parameters:
IKE proposal priority
Encryption algorithm
HMAC
IKE authentication method
DH group
IKE lifetime
When you finish adding IKE policies, click the Next button to proceed to the next task.

## Slide 141: Configuring the Transform Set
Notes: Configuring the Transform Set
The third task in the step-by-step setup is configuring a transform set using the screen shown:
There is a default IPsec transform set that is predefined by CCP. You can use this transform set (and skip Step 2) or add new transform sets.
If you want to use a custom IPsec transform set, create one by clicking the Add button and specifying these parameters:
Transform set name
Encryption algorithm
HMAC
Mode of operation
Optional compression
When finished, click the Next button to proceed to the next task.

## Slide 142: Defining Source and Destination Subnet
Notes: Identifying the Traffic to Protect
There are two options available to define the traffic that you want to protect. You can use the simple mode, allowing protection of traffic between one pair of IP subnets, or you can use an ACL.
Option 1: Simple Mode (Single Source and Destination Subnet)
To protect traffic between a particular pair of IP subnets, follow these steps as shown
Click the Protect all traffic between the following subnets radio button.
Under Local Network, enter the IP address and subnet mask of the local network where IPsec traffic originates.
Under Remote Network, enter the IP address and subnet mask of the remote network where IPsec traffic is sent.

## Slide 143: Defining Interesting Traffic
Notes: Option 2: Using an ACL
Alternatively, you can use an ACL to define a more complex set of proxy identities to protect traffic, as shown:
To specify an IPsec rule that defines the traffic types to protect, follow these steps:
Click the Create/Select an access-list for IPsec traffic radio button.
Click the ... button on the right side of the ACL field to choose an existing ACL or create a new one.
If the ACL that you want to use already exists, choose Select an existing rule (ACL) option. If you want to create a new ACL, choose the Create a new rule (ACL) and select option.
When creating a new ACL to define traffic that needs protection, use the Add a Rule window shown above and follow these steps:
Give the access rule a name and description in the appropriate fields.
Click the Add button to start adding rule entries. The Add an Extended Rule Entry window appears.
The next slide shows the screen you will use to configure a new rule entry:
Under Action, select an action from the drop-down menu and write a description of the rule entry in the Description field.
Each rule entry defines one pair of source and destination addresses or networks. Enter the type, IP address, and wildcard mask for each network under the Source Host/Network and Destination Host/Network sections.
You must use wildcard bits instead of subnet masks.
Optionally, you can provide protection for individual Open Systems Interconnection (OSI) Layer 4 protocols by selecting the required protocol radio button (TCP or UDP) and the required port numbers under Protocol and Service. If the rule applies to all IP traffic, leave the default radio button setting (IP).

## Slide 144: Adding Rules to ACLs

## Slide 145: Configuring a New ACL Rule Entry

## Slide 146: Review the Generated Configuration

## Slide 147: Test Tunnel Configuration and Operation
Check VPN status.
Create a mirroring configuration if no CCP is available on the peer.
Test the VPN configuration.

## Slide 148: Test Tunnel Configuration and Operation

## Slide 149: Remote-Access VPNs

## Slide 150: Teleworking Benefits

## Slide 151: Remote-Access Solutions
There are two primary methods for deploying remote-access VPNs:
IPsec Remote
Access VPN
SSL-Based
VPN
Any
Application
Anywhere
Access

## Slide 152: Remote-Access Solutions
Strong
Only specific devices with specific configurations can connect
Moderate
Any device can connect
Overall Security
Moderate
Can be challenging to nontechnical users
Very high
Ease of Use
Strong
Two-way authentication using shared secrets or digital certificates
Moderate
One-way or two-way authentication
Authentication
Stronger
Key lengths from 56 bits to 256 bits
Moderate
Key lengths from 40 bits to 128 bits
Encryption
All IP-based applications
Web-enabled applications, file sharing, e-mail
Applications
IPsec
SSL

## Slide 153: SSL VPN

## Slide 154: Clientless, Thin Client, or Full Client

## Slide 155: Establishing SSL Session

## Slide 156: Cisco Easy VPN

## Slide 157: Cisco Easy VPN Components
Cisco Easy VPN Server - A Cisco IOS router or Cisco PIX / ASA Firewall acting as the VPN head-end device in site-to-site or remote-access VPNs.
Cisco Easy VPN Remote - A Cisco IOS router or Cisco PIX / ASA Firewall acting as a remote VPN client.
Cisco Easy VPN Client - An application supported on a PC used to access a Cisco VPN server.

## Slide 158: Cisco Easy VPN Exchange

## Slide 159: Configuring Easy VPN Server

## Slide 160: Configuring Easy VPN Server Physical Interface

## Slide 161: Configuring IKE Proposals

## Slide 162: Configuring Transform Set

## Slide 163: Configuring VPN Authentication Method List

## Slide 164: Configuring VPN Authentication Group Policy

## Slide 165: Configuration Summary

## Slide 166: Edit Easy VPN Server

## Slide 167: Easy VPN Server Test

## Slide 168: Connecting Using the Client
R1
R1-vpn-cluster.span.com