# CCNA2 Chapter 10 Practice Test Questions

Which are the first networks to be put in the routing table?

- Directly connected networks.

- Networks learned using OSPF

- Networks learned using EIGRP.

- Networks learned using RIP.

What needs to be true of a link before that link is included in link state updates? (Choose all that apply.)

- The link must have an IP address configured.

- The link must be up.

- The link must be a serial link.

- The link must have its network included in a network command.

Which routing algorithm is used by link state routing protocols?

- DUAL

- SPF

- LSU

- Bellman-Ford

When does a link state routing protocol make most use of bandwidth? (Choose 2)

- It uses a similar amount all the time.

- Every 30 seconds.

- When the routers first start up.

- When the topology changes.

Where does a link state router send link state packets?

- To all directly connected devices.

- To all routers in the area that are running the same routing protocol.

- To one central router in the area.

- To all neighbours with which it has become adjacent.

When does a link state router send hello packets?

- When there is a topology change.

- At regular intervals to maintain a keepalive.

- When a neighbour sends a request.

- To notify that a regular update is due.

Which will be the same for all routers in an OSPF area that has converged?

- The routing table

- The link state database

- The neighbour table

- The best paths to each destination.

What information is included in a link state packet? (Choose all that apply)

- Address and mask of network for the link

- Metric for the link

- Address of final destination network

- Number of hops to destination

- Hostname of neighbour on the link

- Type of link e.g. Serial, Ethernet

Why is it an advantage for a link state protocol to have a hierarchical design?

- It allows routers made by different manufacturers to be used.

- It cuts down processing time and use of bandwidth.

- It allows all routers to become adjacent to each other.

- It allows a more efficient metric to be used.

Which is true of a link state routing protocol?

- Each router should have the same information in its routing table when the network has converged.

- Each router uses the best route metric supplied by its neighbour to calculate backup routes.

- Each router calculates its own best routes using the information in its link state database.

- Each router passes on its best route calculations to its neighbour to save on processing effort.

How does a link state routing protocol differ from EIGRP?

- It uses hello packets to form adjacencies with neighbours.

- It sends updates when the topology changes.

- It is fast to converge.

- It holds information about the whole topology of the routing area.

How do link state protocols manage to avoid routing loops?

- They use the split horizon rule so that they do not send information out of an interface that has received it.

- They hold a complete picture of the topology so that the routing algorithm should not produce any routes containing loops.

- They use holddown timers so that they wait before passing on the information that a link may be down.

- They use count to infinity by restricting the number of hops to a network.

Which are advantages of using a link state routing protocol rather than a distance vector routing protocol such as RIP? (Choose 2)

- Link state routing protocols give fast convergence.

- Link state routing protocols make lower demands on router processing power.

- Link state routing protocols send regular complete updates so that the information is always correct.

- Link state routing protocols tend to use less bandwidth after the initial flooding phase.

What is the Dijkstra algorithm?

- Another name for the Bellman-Ford algorithm.

- Another name for the DUAL algorithm.

- Another name for the SPF algorithm.

- Another name for the STP algorithm.

Which is true of OSPF’s metric in the Cisco implementation?

- The metric is cost, which is calculated so that the highest bandwidth links have the lowest cost.

- The metric is cost, which is calculated using the number of hops.

- The metric is cost, which is calculated according to the charge that the ISP makes for the link.

- The metric is cost, which is calculated using bandwidth and delay by default, though load and reliability can also be used.

When a link goes down, how long does a router running a link state protocol wait before sending an update to its neighbours?

- 30 seconds

- 90 seconds

- 30 minutes

- It sends the update at once.

What does a link state router do to a link state packet after receiving it and before forwarding it to a neighbour?

- It updates the metric by 1.

- It recalculates the best routes and updates the packet.

- Nothing. It forwards the packet as it is.

- It does not forward packets that it receives.

Where would OSPF be a good choice of routing protocol but EIGRP would not?

- On a network where the routers are old and have little processing power.

- On a network where non-Cisco routers may be used.

- On a network where subnetting uses VLSM.

- On a network where fast convergence is essential.